## Slide 1: CENTRAL SCADA SYESTEM OVERVIEW OF SAVAR-KERANIGANJ WELLFIELD PLANT DHAKA WASA PRESENTED BY MASHUDUL ALAM, EXECUTIVE ENGINEER DATE: JANUARY 25, 2022.

## Slide 2
OBJECTIVE
Supply 150 MLD i.e. 15 Cr. Liter Safe Potable Water Daily to Mitigate Water Scarcity in Mirpur Area.

## Slide 3: MAJOR INSTALLATIONS & FACILITIES

## Slide 4: MAJOR INSTALLATIONS & FACILITIES (CONT.)

## Slide 5: LOCATION MAP OF DTWS

## Slide 6: PLANT PROCESS - BLOCK DIAGRAM

## Slide 7: DEEP TUBE WELL (DTW)
46 no’s DTWs;
IRP#1:23 no’s, IRP#2: 23 no’s
Pump Design Head: 60m
Pump Design Flow: 204 m3/h
Pump Motor Power: 55kW
The Source of Raw Water for the Iron Removal Plant

## Slide 8
IRON REMOVAL PLANT (IRP)
Divided into 5 Main Parts:
Cascade Aerator
Sedimentation Tank
Rapid Sand Filter

## Slide 9
IRON REMOVAL PLANT (IRP)
Divided into 5 Main Parts (Cont.):
Backwash Water Holding Tank
Sludge Drying Bed

## Slide 10: CHLORINATION SYSTEM
3 no’s Chlorinator (2 in Duty + 1 standby)
Max. Dosing Capacity: 20 kg/hr.
18 no’s Cylinder (Each Capacity: 1,000 kg)
For Disinfection of Filtered Water

## Slide 11: NEUTRALIZATION PLANT
Chlorine: Poisonous Gas
Chlorine Leak Detection System
Caustic Soda (NaOH) for Chlorine Neutralization
2NaOH + Cl2 = NaOCl + NaCl + H2O

## Slide 12: OVER GROUND RESERVOIR (OGR)
Divided into 2 parts
Each Size: 42.3x20x5 m
Water Holding Capacity: 2x4,230 m3 = 8,460 m3
Stores Treated Water from IRPs.

## Slide 13: DISTRIBUTION PUMP
Pumps Treated Water to Transmission Network
Double Suction Centrifugal Pump
6 Sets (4 Duty+2 Standby)
Each Design Capacity: 1,600m3/hr.
Each Design Head: 45m
Motor Power Rating: 280kW

## Slide 14: TRANSMISSION NETWORK
13.2 km Long Transmission Network
Pipe Diameter: 1200mm to 600mm
13 no’s Nodal Points with Chambers
Air Release Valve: 13 no’s
Butterfly Gate Valve: 5 no’s
Wash Out: 3 no’s

## Slide 15: CENTRAL SCADA SYSTEM
Savar Keraniganj Wellfield Plant
is the most modern water Iron Removal Plant of Dhaka WASA.
Dhaka WASA Central SCADA system is developed day by day, following the foundation of Savar keraniganj wellfield Plant SCADA system.

## Slide 16: MOST ADVANCED SCADA SYSTEM SAVAR KERANIGANJ WELL-FIELD PLANT(SKWP)
Fully Automated System using AI
Latest Technology
Cost Free Communication Between NOC to RTU

## Slide 17: MOST ADVANCED SCADA SYSTEM SAVAR KERANIGANJ WELL-FIELD PLANT(SKWP)
Redundant PLC
Redundant Server
Dual Ring Topology

## Slide 18: MOST ADVANCED SCADA SYSTEM SAVAR KERANIGANJ WELL-FIELD PLANT(SKWP)
Plant Based Equipment Parameter
Ultrasonic Flow Indicator Transmitter
Ultrasonic Level Transmitter
Pressure Indicator Transmitter
Variable Frequency Drive
Uninterrupted Power Supply
Under Voltage Relay
Earth Leakage Detector
Radio Communication
Motor Operating Valve (MOV)
Generator Status
Electrical System Monitoring
Chlorine Dosing System
Etc.

## Slide 19: MOST ADVANCED SCADA SYSTEM SAVAR KERANIGANJ WELL-FIELD PLANT(SKWP)
DTW Based Equipment Parameter
Remote Terminal Unit
Flow Indicator Transmitter
Level Indicator Transmitter
Pressure Indicator Transmitter
Variable Frequency Drive
Uninterrupted Power Supply
Under Voltage Relay
Earth Leakage Detector
Radio Communication
Generator Status
Electrical System Monitoring
Etc.

## Slide 20: CLEAR SCADA SYESTEM OVERVIEW

## Slide 21: OVERVIEW

## Slide 22: DEEP TUBE WELL 1-12

## Slide 23: SAND FILTER IRP-1

## Slide 24: SAND FILTER IRP-2

## Slide 25: SLUDGE DRYING BED

## Slide 26: OVER GROUND RESERVOIR
Booster Pump

## Slide 27: CHLORINE DOSING SYSTEM

## Slide 28: ELECTRICAL SYSTEM

## Slide 29: AUTOMATICALLY GENARATED REPORTING SYSTEM

## Slide 30: CONCLUSION
Why is automation necessary?
Advantages commonly attributed to automation include higher production rates and increased productivity, more efficient use of equipment's, better product quality, improved safety, shorter workweeks for labor, and reduced factory lead times. Worker safety is an important reason for automating an industrial operation.
How is automation useful in future?
Automation has shown significant progression and that is now consistently present in various fields. There are ongoing concerns that automation will replace jobs in some industries; however evidence suggests it can also create new jobs and steer people towards other opportunities.

## Slide 31: THANK YOU